## Slide 1
Inverse Problems: THz- and phase space tomography and machine learning
Andrea Santamaria Garcia, Erik Bründermann, Stefan Funkner,
22 Nov 2021, 13:30-17:35
Mathematik in der Teilchen- und Astroteilchenphysik:
Diskussion zukünftiger Zusammenarbeit und Identifikation gemeinsamer Projekte

## Slide 2: Particle accelerators – one of the most complex machines in the world!
Magnet systems
Radiofrequency cavities
Diagnostics
Vacuum
Cryogenics
Detectors
A feat of enginering
for applied research
(and industry, medicine)
R&D
Users (experiments)
The Karlsruhe Research Accelerator (KARA)
currently more than 30,000 accelerators in operation around the world

## Slide 3: Particle accelerators – one of the most complex machines in the world!
The Karlsruhe Research Accelerator (KARA)
Minimum mean time between failures
  Prevention / early detection / fast interventions
Minimum time to set-up & optimize operation modes
Goal for any accelerator:
maximum availability
= useful beamtime

## Slide 4: Fault detection to increase availability
The fault detection problem
Isolation
What type of fault has happened (explainability)
Estimation
What is the magnitude of the failure (non-functional or functional in a degraded state?)
Alarm
Labeling an event as faulty or normal (binary classification)
Model-based fault diagnosis:
Model
Observed signal
used to identify faults
=
-
residual signal
The majority of the time we don’t have a model
Models are always approximations
discrete Kalman filter eq.

## Slide 5: Data-driven methods for fault detection
Challenges
Data asymmetry
Heterogeneity of the failure types
Data sampling rate
Date | Description
12.04.2021 | BPM restart loop
22.10.2020 | Sudden variation of BPM charge button
16.10.2019 | Sudden variation of BPM charge button
06.09.2019 | Faulty fan in BPM cooling system
04.09.2019 | BPM RAM usage warning
28.10.2016 | No data readout
BPM = Beam Position Monitor
Autoencoder neural network
Latent space
Sparse representation focusing on key properties
Input data
Normal operation data
(no failures)
Output
Loss threshold
Anomaly would be above threshold

## Slide 6: Data-driven methods for fault detection
Autoencoder neural network
Latent space
Sparse representation focusing on key properties
Input data
Normal operation data
(no failures)
Output
Loss threshold
Anomaly would be above threshold
Which accelerator signals are correlated and are relevant to the device failure?
Feature selection & crafting
Time series analysis
Data cleaning
Which time interval is representative?
How to normalize different signals?
Autocorrelation, seasonality, stationarity
Segmentation, smoothing, signal estimation
Based on domain knowledge

## Slide 7: Data-driven methods for fault detection
Which accelerator signals are correlated and are relevant to the device failure?
Feature selection & crafting
Time series analysis
Data cleaning
Which time interval is representative?
How to normalize different signals?
Autocorrelation, seasonality, stationarity
Segmentation, smoothing, signal estimation
Based on domain knowledge
Important for any machine learning method
Notes: Causal analysis

## Slide 8: The final challenge
“The curse of dimensionality” or Hughes phenomenon
ML method
Classifier
Regressor
Fixed number of data samples
Sparse data
Predictive power
Number of features
Clustering becomes impossible because the distance of observations appears equal
Accelerators have hundreds of thousands of not-so-statistically-significant signals
Feature selection / dimensionality reduction is key