## Slide 1
MDC architecture (Brainstorming)
Michele Caselle
PANDA DAQ FEE Workshop, 6-7 October, 2021

## Slide 2
Hybrid silicon pixel
  10 million pixel
  2 barrel layers + 6 disks
Silicon micro-strip
  200,000 strip channels
  296 sensors
  2 barrel layers + 2 disks
  312 strip modules (Barrel)
  48 strip modules (Disk)
Micro Vertex Detector of PANDA
The innermost detector for precise tracking and detection of primary and secondary vertices
40 cm
p
target
Notes: The Micro-Vertex Detector (MVD) as the innermost part of the tracking system will enable precise tracking and detection of primary and secondary vertices. It is equipped with both silicon pixel and strip sensors.

## Slide 3
Barrel
  # 64 square sensor modules readout by 8 ToASt each
  # 184 rectangular sensor modules readout by 11 ToASt each
Silicon Strip Detector
Complex detector modules for both barrel and disk
Disk
  # 48 trapezoidal sensor modules readout by 12 ToASt each
Silicon sensor
ToASt front-end chip
Carbon fiber support
Module Data Concentrator
ASIC
# 296 MDCs are foreseen to transmit the data to the GBTX (or LpGBT) by e-link (320 Mb/s) interface
# 30 GBTs are foreseen to readout the entire strip detector by optical links (to off-detector electronics)

## Slide 4
Design completed in UMC 110 nm by INFN-Turin
Triple modular redundancy (TMR) logic protection
Submitted on April, 28th , 2021
HDL model still in preparation (Gianni)
Silicon Strip Detector
Status of ToASt front-end ASIC
50
ToAST manual + material on our indico:
https://indico.scc.kit.edu/category/124/

## Slide 5
  Developed in UMC 110 nm CMOS technology
  Digital logic based on Triplicated Modular Redundancy (TRM) for Single Event Upset mitigation (registers, memories and FSMs)
  First implementation on FPGA to prove the digital behaviour
  Electrical test by HghFlex 2 (HW platform)
Optical link
ToASt
ToASt
…
ToASt
GBT
Module Data Concentrator (MDC) ASIC
Detector timing & controls
…
…
MMB
(MVD Multiplexer Board)
sensor
Module Data Concentrator (MDC) - ASIC
Architecture
Notes: (consolidated experience at KIT, collaborations synergies with PSI and INFN-TO)

## Slide 6
ToASt
ToASt
…
ToASt
Detector timing & controls
sensor
Module Data Concentrator (MDC) - ASIC
Architecture
  Only HDL codes (no IPcores)
  Reduce the logic as the minimum possible ( no large memories user-space, limited number of states for FSM
  Triplicated Modular Redundancy (TRM) for Single Event Upset mitigation (registers, memories and FSMs)
  Power consumption as low as possible

## Slide 7
Module Data Concentrator (MDC) - ASIC
Current status and what’s next
Module Data Concentrator (MDC) ASIC
Optical link
ToASt
ToASt
…
ToASt
GBT
Detector timing & controls
…
…
MMB
(MVD Multiplexer Board)
Moving “Feature Extraction” data processing on more flexible programmable logic (FPGA)
More flexibility, leveraging the ASIC design and more intelligent (ML) data processing on FPGA
…
Notes: (consolidated experience at KIT, collaborations synergies with PSI and INFN-TO)

## Slide 8
Module Data Concentrator (MDC) - ASIC
ToASt
ToASt
…
ToASt
Detector timing & controls
  HIGH PRTIORITY
  Front-end interface (SerDes, bitslip, 8b/10b decoding)
  Intelligent multiplexer, only the active and working channels must be readout
  We need the FPGA implementation of the E-port, for now (by CERN ?)
Clock from GBT
Data-up (160 Mb/s)
Data-down
Notes: (consolidated experience at KIT, collaborations synergies with PSI and INFN-TO)

## Slide 9
Module Data Concentrator (MDC) - ASIC
ToASt
SerDer
Bitslip
160 Mb/s
Two output serial links
Tx_1
Tx_2
SerDer
10b/8b
10b/8b
Zero-suppresion
Zero-suppresion
Small FIFO
Small FIFO
10 bit
8 bit
Only data with hit
ToASt
SerDer
Bitslip
160 Mb/s
Two output serial links
Tx_1
Tx_2
SerDer
10b/8b
10b/8b
Zero-suppresion
Zero-suppresion
Small FIFO
Small FIFO
MUX
CRC correction
logic
empty
Priority encoder

## Slide 10
Module Data Concentrator (MDC) - ASIC
ToASt
SerDer
Bitslip
160 Mb/s
Two output serial links
Tx_1
Tx_2
SerDer
Small FIFO
Small FIFO
32 bit
Small FIFO
Small FIFO
MUX
ECC error correction
code
logic
empty
Priority encoder
On case of:
NO 8b/10b
No zero-suppression
ToASt
SerDer
Bitslip
160 Mb/s
Two output serial links
Tx_1
Tx_2
SerDer
32 bit
ECC error correction
code
Sync code: 00 00 1100 1100 1100 1100 1100 1100 1111

## Slide 11
Backup slides

## Slide 12
Proposed DC-PANDA based on ZYNQ
Very-flexible, heterogenous and high-performance back-end
** Module Management Controller
SODANET
ETH (up to 100 Gb/s)
To server Node
Up to #34 GBTs
(from/to detector)
…
DDR4
Udimm
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
AMC backplane
PLL
LMK04610
…
US+
Zynq
16 x LVDS
X 4 PCIe
X 2 GbE
IPMI*
*Intelligent Plattform Management Interface
RoCE
SATA (opt.)
Protocol on the AMC-backplane
  Up to 60 optical links from/to GBTs still possible
  Up to 100 Gb/s ETH (upstream) + an additional 100Gb/s as spare
  Fully compilated AMC-backplane connections including 2 x GbE , 4 x lanes PCIe, 2x SATA and IPMI on ARM processors  dramatic reduction of the necessary firmware (FPGA) for the implementation of the AMC protocols
Notes: Module management controller (MMC)

## Slide 13
Proposed MMB for MVD
Optical links - details
SODANET
ETH (up to 100 Gb/s)
To server Node
Up to #34 GBTs
(from/to detector)
…
DDR4
Udimm
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
AMC backplane
PLL
LMK04610
…
MMC**
ATMega328P
US+
Zynq
16 x LVDS
X 4 PCIe
X 2 GbE
IPMI*
RoCE
SATA (opt.)
Protocol on the AMC-backplane
SODANET
ETH (up to 100 Gb/s)
To server Node
GBTs
(up to 24 links)
…
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
PLL
LMK04610
…
US+
Zynq
RoCE
FireFly Tx/Rx
spare
FireFly Tx/Rx
ETH spare
FireFly Tx/Rx
X10 links as spares
Optical fibers front-panel detail
Spares fibers
Not used optical fibers in power-saving modes
Dynamic reconfiguration of the transceivers by ARM processor and not by FPGA
4 x 25 Gb/s FireFly

## Slide 14
Data flow from the detector to compute node fully independent from the ARM processes
ARM could process the incoming detector data without disturb the main data flow
MMB at the experimental area
Advantages of the ZYNQ – ARM processor for the MVD
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
FireFly Tx/Rx
…
Data Receivers
FPGA
Processing
Data Transmitters (ETH)
FPGA
ARM cores
Processors systems
Data check
From
detectors
To Compute Node
On-line Data Quality Monitoring and Anomaly Detection
GbE
TCP/IP
AXI interconnect
Quality of the data =
Quality of the physics results

## Slide 15
Silicon Strip Detector
Readout architecture
FEE- ASICs
Local controller ASICs
Compute node cluster
Double-sided strip modules
ToASt
ToASt
ToASt
…
MDC
(Module data Concentrator)
ToASt
ToASt
ToASt
…
MDC
(Module data Concentrator)
GBT
e-links
GBT
e-links
ToASt
ToASt
ToASt
…
MDC
(Module data Concentrator)
ToASt
ToASt
ToASt
…
MDC
(Module data Concentrator)
GBT
e-links
GBT
e-links
Sensor
…
Outside active volume
Counting room
(Real-time)
…
…
SODANET
MMB
(MVD Multiplexer Board)
MMB
(MVD Multiplexer Board)
optical link
Ethernet switch / InfiniBand
On-line
(off the shelf devices)
Server node
Server node
Server node
Server node
Server nodes equipped with commercial and powerful hardware (CPU/GPU/FPGA)
…
Permanent storage
Downlink (controls & timing)