## Slide 1: Only for internal discussion

## Slide 2: Full readout chain simulated
MDC
320 MHz
ToASt
ToASt
ToASt
160 MHz
TX_0
TX_1 (150 Mb/S)
12 ToASt
LpGBT (320 Mb/s)
Data Acquisition
MMC (FPGA)
Data Consistency Check
Simulator dispay
Verilog emulator of the ToASt (by Michele), event generator by random generator @ 2MHz
Verilog code of MDC – ASICs (full readout chain based on simple Round – Robin)
SERDES stage with bitslip align.
Async. Channel FIFO + FSM control
Main FSM readout control
Main Async. FIFO
Serializer FSM (320 Mb/s)
Verilog code of MMD
Receiver SERDES stage with bitslip align.
Main FSM readout control
Data Consistency Check

## Slide 3: MDC architecture
ToASt
SERDES
FSM align
bitslip
FSM
Control
Async.
FIFO
FSM
Readout
lock
ToASt
SERDES
FSM align
bitslip
FSM
Control
Async.
FIFO
32 x 64
FSM
Readout
lock
ToASt
SERDES
FSM align
bitslip
FSM
Control
Async.
FIFO
FSM
Readout
lock
… x 12 ToASt
MUX
intelligent Round-Robin controller
Main FSM
2x 160 Mb/S
Frame alignment check
Trailer check
5 MHz
40 MHz
@ 40 MHz
Async.
FIFO
32 x 1024
FSM
E-link
320 Mb/s
To LpGBT
40 MHz
320 MHz

## Slide 4: Special features
Readout channel:
  In case of channel not locked  logic in shutdown (low-power)
  Only if the channel is locked  it will be readout
   one MDC ASICs compatible for all detectors modules (barrel + disks)
Main architecture
  Simple readout mplementation

## Slide 5: What is missing
Readout channel:
  CRC implementation and strategy in case of errors
  Possible evolution from pure Round-Robin  quasi-priority based on the FIFO channel occupancy, this will reduce the risk of FIFO_full, should reduces the FIFO size, should improves the detection of clusters
  …to be check the possibility to set the clock phase foreach ToASt link
Main architecture
  Possible evolution from Round-Robin  quasi-priority
  Replacement of the e-link logic with 8b/10b encoder