## Slide 1
KIT accelerators and research highlights - an overview
Bastian Härer on behalf of the KIT team

## Slide 2: The Accelerator Technology Platform @KIT (ATP)
  5 divisions
  6 KIT facilities
  14 institutes
  Helmholtz
  3 research fields
  6 programs
  The Research University in the Helmholtz Association
  + strong
  industrial partners
ATP in
lookKIT
(German)

## Slide 3: Test facilities & technologies - examples
Winding technologies
Pulse power technology Gyrotrons
Cable technologies High temperature superconductors
Magnet test facilities

## Slide 4: Accelerator & energy systems Test field KITTEN
model
control
simplify
implement
Courtesy: Giovanni De Carne,
Head of „Real Time System Integration“, KIT
real-time simulator
time-efficient
real-time model
mathematical model
energy-informed &
physics-informed
digital twin of KARA
Digital twin of KARA
  Analyzing, developing and testing future energy solutions for research infrastructures
InnovEEA
  Load management (grid stability)
COLLAGE: ANKE-SUSANNE MÜLLER, FOTO : MARKUS BREIG

## Slide 5: Karlsruhe Research Accelerator (KARA)
KIT synchrotron light-source & accelerator test facility
www.ibpt.kit.edu/kara
Courtesy: U. Herberger
Parameters | Values
Circumference | 110.4 m
Energy range | 0.5 – 2.5 GeV
RF frequency / period | 500 MHz / 2 ns
Revolution frequency / period | 2.715 MHz / 368 ns
Beam current | up to 200 mA
RMS bunch length | 45 ps (2.5 GeV) a few ps (1.3 GeV)
FCC-FS
FCCIS

## Slide 6: KARA Operation Status
Operation modes in 2022:
  0.5/2.3/2.5 GeV user optics, 0.5/1.3 GeV low-alpha, 0.5/1.3 GeV negative alpha
Power supply refurbishment program
  Replaced Booster main power supplies
    Direct EPICS control interface on device
    Continuous operation at all energies (50 – 500 MeV)
  Replaced KARA dipole power supply (800 A / 520 V)
    Direct EPICS control interface on device
    Enable new operation modes like down ramping
  New KARA quadrupole power supplies in the ordering process
    Start with family powering
    Test individual powered quadrupole magnets
  Installed new PS for KARA sextupole magnets and split them from two into tree families
Booster Dipole PS
(1000 A / ±240 V)
Booster Quadrupole PS
(120 A / ±108 V )
Picture: H. Hoteit

## Slide 7: Impedance manipulation at KARA
Goal: Observe, understand, and control the microbunching instability
Corrugated plates will be installed at KARA
Affecting threshold current and/or bursting frequency with additional impedance
S. Maier et al. https://doi.org/10.18429/JACoW-IPAC-23-WEPL189

## Slide 8: EO Near-Field @ KARA: Phase Space Tomography
single-bunch @ 2.7 MHz
S. Funkner et al., Sci Rep, March 2023, Vol. 13.1, pp. 1-11. doi:10.1038/s41598-023-31196-5
revolution plots/ sinograms
phase space density
Phase space tomography
Complete phase space image reconstructed from time interval of 61 μs
“Randon morphing“ between independent measurements
05K22VKB
05K19VKD
S. Funker et al., Sci. Rep. 4618 (2023) https://doi.org/10.1038/s41598-023-31196-5

## Slide 9: EO Near-Field @ KARA: Towards Multi-Bunch Measurements
Prototype for an EO Bunch Profile Monitor for FCC-ee:
First 2 bunch EOS measurements at KARA:
Compensation for signal drift (heating?)
Two bunches are clearly visible in the measurement
M. Reißig et al. https://doi.org/10.18429/JACoW-IPAC2023-THPL121

## Slide 10: FLUTE: Accelerator Test Facility at KIT
Final electron energy | ~ 41 | MeV
Electron bunch charge | 0.001 - 1 | nC
Electron bunch length | 1 - 300 | fs
Pulse repetition rate | 5 | Hz
THz E-Field strength | up to 1.2 | GV/m
FLUTE (Ferninfrarot Linac- Und Test-Experiment)
  Test facility for accelerator physics within ARD
  Experiments with THz radiation
Courtesy: S. Schott
www.ibpt.kit.edu/flute
R&D topics
  Serve as a test bench for new beam diagnostic methods and tools
  Systematic bunch compression and THz generation studies
  Develop single shot fs diagnostics
  Synchronization on a femtosecond level

## Slide 11: : upgrade status
Parameter | Value
Input RF power | 9.5 MW
Output Energy | 5.5 MeV
Operating Frequency | 2.998 GHz
Repetition rate | 50 Hz
Peak cathode field | 120 MV/m
Bunch charge (max) | 1 nC
Dedicated RF units for RF photo-injector and linac have been installed and commissioned
New RF photo-injector with low dark current has been delivered, installation and commissioning is under way
Installation of the RF waveguide for the linac and its conditioning will follow
UV laser beam aligned and referenced
RF photo-injector
Solenoid
Diagnostic section
K100 waveguide
Circulator
K100 RF unit (10 MW)
K300 waveguide
K300 RF unit (37 MW)
Linac
Courtesy: S. Schott

## Slide 12: Controlling the Transverse Beam Shape of the Photoinjector Laser via an SLM
Evolve last year’s test setup and approach by ...
  Using the Ti:Sa 800 nm photoinjector laser system
  Including a compressor in the optical path
  Mapping the camera intensity directly to the phase modulation via a deep neural network
Head: Conv2D
Tail: Dense
Camera images
Size: 100x100
Zernike
Amplitudes
Head: Conv2D
Body:
EfficientNetV1B1
Tail: Dense
Schematic setup
Neural network architecture
Test results

## Slide 13: Split-ring resonator
Streaking with THz radiation and amplifying the electric field with a 20 µm gap split-ring resonator
Illustration
Optical setups
Setup of the split-ring resonator measurement in low energy section at FLUTE
Experimental setup in vacuum chamber installed and in commissioning
20 mm
Courtesy: S. Schott
© Katja Heil, IBPT
J. Schäfer et al. https://doi.org/10.18429/JACoW-IPAC-23-THPL122 M. Nabinger et al. https://doi.org/10.18429/JACoW-IPAC-23-THPA079

## Slide 14: Accelerator technology for precision medicine
KARA  photon irradiation
FLUTE  electron irradiation
First tests in cooperation with DKFZ
Hydrogel
Lab, AK Schepers, KIT - IFG
water equivalent plates
e-
Courtesy: C. Stengl, S. Schott
KIT Center HealthTech Development and implementation of innovative technologies leading to the transformation of health technologies into future healthcare.
https://www.healthtech.kit.edu/
K. Mayer, Master thesis 2023

## Slide 15: cSTART Project
Motivation: Storage of ultra-short (fs) electron bunches with high repetition rate
Compact storage ring with very large momentum acceptance and dynamic aperture
FLUTE with new transfer line as injector
Status:
  Conceptual design and specification: finished
  Transfer line magnets: first magnets delivered
  Test diagnostics at KARA booster: ongoing
y / m
x / m
Circumference | 43.2 m
Energy | 50 MeV
Revolution time | 144 ns; 6.9 MHz
Storage time | 100 ms
A. Papash et al. https://doi.org/10.18429/JACoW-IPAC2022-THPOPT023
M. Schwarz et al. https://doi.org/10.18429/JACoW-IPAC-23-WEPL167
D. El Khechen et al. https://doi.org/10.18429/JACoW-IPAC2022-MOPOPT026 J. Schäfer et al. https://doi.org/10.18429/JACoW-IPAC2022-MOPOST041 B. Härer et al. https://doi.org/ 10.18429/JACoW-IPAC2022-THPOPT059

## Slide 16: KARA Booster Diagnostics
Injection facility for KARA
Components:
  53 MeV racetrack microtron
  Injection line
  26 m circumference booster synchrotron (53 MeV → 500 MeV, RMS bunch length: 200 ps...1000 ps)
  Extraction line
Diagnostic Devices:
  Button/Stripline beam position monitors
  Two synchrotron radiation ports
Implement longitudinal diagnostics to improve storage ring injection efficiency
Preliminary results,
scan using hexapod system:
M.-D. Noll et al. https://doi.org/10.18429/JACoW-IPAC2023-THPL126
⌀ 62 micro-meter

## Slide 17: Longitudinal beam dynamics for different initial distributions at cSTART
Contain 40 % of particles
Survive for 100 ms
RMS bunch length ≤ 1 ps
Initial distribution
Distribution after 100 ms
M. Schwarz et al. https://doi.org/10.18429/JACoW-IPAC-23-WEPL167
Sub bunches
Storage time ≪ damping time → Non-equilibrium dynamics
Simulation of 700 k turns with 1 M macro-particles
1 pC
fs;

## Slide 18: @KIT - Status
LPA
intersection dipole
LPA plasma cell
Clean room for laser system built ✓
Commercial laser system in commissioning
Conceptual design of transfer lines including diagnostics finished ✓
Next step: Fine-tuning of optics and tracking calculations
Additional professor at KIT in 2023
Courtesy: S. Jalas, M. Kirchen, DESY
Goal: injection & storage of a laser plasma accelerator beam in a storage ring

## Slide 19: AI4Accelerators team highlights
Reinforcement Learning
Bayesian Optimization
First successful application of RL in an accelerator with online training and running on hardware in the world at KARA!
Time to inject to KARA cut in half with automated tuning by BO algorithm
Emitted THz radiation at FLUTE optimized with parallel BO in simulation
Transfer of algorithm to EuXFEL to tune SASE emission
Lattice agnostic RL
Code usable in different accelerators
https://doi.org/10.1103/PhysRevAccelBeams.26.034601
https://doi.org/10.18429/JACoW-IPAC2022-WEPOMS023
https://www.ipac23.org/preproc/pdf/THPL028.pdf
https://arxiv.org/abs/2306.03739
RL vs BO
Creation of the Collaboration on Reinforcement Learning for Autonomous Accelerators (RL4AA)!
Kick-off with workshop organized at KIT
Proceedings to be published
https://rl4aa.github.io/

## Slide 20: Lattice-Agnostic Reinforcement Learning Control
C.Xu, IPAC23-THPL029
Goal: train a generalisable RL agent for transverse control
Method: extends the domain randomization (DR) in training, change magnet positions in each episode
Result: in simulation, the DR-agent could perform the task zero-shot; with only 2% fine-tuning steps it recovers the full performance.
The trained RL agent could perform the tuning task at ARES-EA fast and accurately.

## Slide 21: Technology transfer from KARA to the world
Superconducting Undulators – The future is now
Bilfinger Website: “Superconducting undulators … most powerful light source for any experiment”
USA
NSLS-II@BNL
3 GeV SCW
Australia
Synchrotron, Melbourne
ANSTO - BioSAXS beamline
2022
2020
EuXFEL
SCUs for FELs
2020
© Bilfinger Noell GmbH
© Bilfinger Noell GmbH
First light: Nov. 2022
First light: Nov. 2022

## Slide 22: HTS magnet technology
HTS miniature magnets
HTS compact undulator
Main challenges: Bending radii < 5 mm
Quench protection
VR and hel. prototype coils were manufactured and successfully tested
Successfully tested in LN2 at 77 K
HTS tape
iron
periodic quadrupole
Demonstrator - HTS windings in 72 turns
- iron core
I = 1.3 kA at 4.2 K, gmax = 170 T/m

## Slide 23: Acknowledgements
The accelerator team
Falastine Abusaif, Axel Bernhard, Edmund Blomley, Simon Braner, Erik Bründermann, Hyuk Jin Cha, Kantaphon Damminsek, Dima El Khechen, Samira Fatehi, Stefan Funkner, Julian Gethmann, Christian Goffing, Andreas Grau, Leander Grimm,Steffen Grohmann, Bastian Härer, Michael Hagelstein, Erhard Huttel, Igor Kriznar, Stephan-Robert Kötter, Bennet Krasch, Anton Malygin, Sebastian Maier, Sebastian Marsching, Yves-Laurent Mathis, Katharina Mayer, Wolfgang Mexner, Matthias Nabinger, Michael J. Nasse, Gudrun Niehues, Marvin Noll, Alexander Papash, Meghana Patil, Micha Reißig, Robert Ruprecht, Andrea Santamaria Garcia, Patrick Schreiber, David Seaz de Jauregui, Jens Schäfer, Thiemo Schmelzer, André Schmidt, Marcel Schuh, Markus Schwarz, Nigel John Smale, Johannes L. Steinmann, Pawel Wesolowski, Christina Widmann, Chenran Xu and Anke-Susanne Müller
KIT Partner Institutes (ETP, IHM, IMS, IPE, IPS, LAS, IAR, IPQ)
Collaboration partners:
Thank you for your attention!
Felipe Donoso Aguirre,

## Slide 24: EO diagnostics at IBPT
Resolving electron bunch profile in every turn @ 2.7 MHz
Capable of uninterrupted data acquisition for up to several millions of turns
First measurements with two bunches
Section of a measurement dataset of 100000 turns
Near-field:
Off-line demonstrator:
Far-field:
Experiment under commission, status: successful EOS demonstration with off-line demonstrator using balanced detection
Aiming to measure the complete THz pulse in single-shot
Presentation by A. Schmidt
Presentation by M. Reißig
Presentation by L. Grimm

## Slide 25: Bayesian Optimization for SASE at EuXFEL
C.Xu, IPAC23-THPL028
Applied Bayesian Optimization (BO) for FEL pulse energy tuning
  Tune up to 10 air-coil correctors at SASE1 Beamline
  Plug-and-play implementation (operator friendly), automatic hyperparameter determination at runtime
  Comparable performance as the daily tuning tool in OCELOT optimizer (Nelder-Mead simplex), but faster and smoother convergence
Code available at: https://github.com/cr-xu/bo-4-euxfel

## Slide 26
Development of world first superconducting undulator in the THz regime
In cooperation with industrial partner Bilfinger Noell (BNG)
Target photon frequencies of 1st harmonic: 4 THz (15.5 meV) – 12 THz (50 meV)
New technology and transfer – THz undulator for FLUTE
  Period length 65 mm
  Magnetic gap 40 mm
  peak magnetic field 0.88 T
  Nominal current main coils to reach field IMC = 355 A
  Number of full periods 14.5 (overall length 1800 mm)
Magnet design:
Project status:
  CDR finished
  TDR ready in summer 2023
  Magnets produced till end 2023