## Slide 1: Emittance exchange options for injectors
Jonas Kallestrup :: Paul Scherrer Institute
I.FAST Workshop on Injectors for Storage Ring Based Light Sources Karlsruhe, 7.-8. March 2024

## Slide 2: Why emittance exchange?
Horizontal off-axis injection requires an acceptance of:
booster synchrotron as injector
  large due to large
  small not optimum for injection into horizontal dynamic aperture
If we can exchange with then required becomes smaller!

## Slide 3: Generalized emittance exchange
Objective: create system with transfer matrix such that transverse emittances of the beam are perfectly exchanged:
How must look?

## Slide 4: Ways of doing emittance exchange Transfer lines

## Slide 5: Emittance exchange transfer line exchange
Clever arrangement of skew quadrupoles will exchange emittances
  Maybe the oldest method: proposed in 1970!
Simple. Clean. Stable.
Must be kept dispersion-free to avoid vertical dispersion after exchange.
CERN proposal: 3 skew quads + interleaved normal quads 90° phase advance.
BESSY proposal: 5 skew quads

## Slide 6: Emittance exchange APS-U BTS transfer line exchange
Thanks to Michael Borland for the lattice

## Slide 7: Ways of doing emittance exchange Resonances in boosters

## Slide 8: Emittance exchange using resonances Terminology
Resonance condition for linear difference resonance: integer
Betatron tune separation / “detuning”:
  ^hat indicates fractional part of tune
Coupling coefficient of linear difference resonance:
  “natural” from rotated quadrupoles and vertical offsets in sextupoles, etc.
  “induced” from by pulsed skew quadrupole
Dotted lines act as “stop-band” for and
Experimentally measurable tunes are the “normal-mode tunes”:

## Slide 9: Emittance oscillations due to linear difference resonance
.016
.064
No damping!

## Slide 10: Emittance oscillations due to linear difference resonance
.016
.064
With damping!
static equilibrium

## Slide 11: Emittance sharing the easy choice
0.32 0.29
0.29
Nice and slow – easy for power supplies
But this is just equalizing the emittances! How to improve the situation??

## Slide 12: Emittance exchange coupling resonance crossing
Crossing the resonance can lead to emittance exchange
  Only spend time within the stopband when you need it!
    Example
0.25 0.35 0.25
“Free” if the coupling in the machine is non-zero and quadrupole power supplies are capable of ramping with the required speed
Damping deteriorates the exchange
  Works best for machines with long

## Slide 13: Emittance exchange SLS booster coupling resonance crossing
Preparations for resonance crossing: investigate the state of the SLS booster
  Measure tunes along ramp
  Coupling coefficient measured by closest tune approach by scanning QF family current
Resonance crossing possible by decreasing QF-family current before extraction
Page 13

## Slide 14: Emittance exchange SLS booster coupling resonance crossing
is reduced to ease resonance crossing
Rapid tune-shift within last 2.4 ms before extraction
Page 14

## Slide 15: Emittance exchange SLS booster coupling resonance crossing
From quadrupole scans:
Limited by

## Slide 16: Emittance exchange Resonance crossing elsewhere
Sirius booster
exchange
Inj. Eff:
doi:10.18429/JACoW-IPAC2021-MOPAB051
ESRF-EBS booster
Inj. Eff:
doi:10.18429/JACoW-IPAC2021-MOPAB051
Elettra booster
Est. Elettra-2 Inj. Eff.: 87%
doi:10.18429/JACoW-IPAC2023-WEPL022

## Slide 17: Emittance exchange SLS booster coupling resonance crossing
From quadrupole scans:
How to improve?
Reduce by further decoupling the machine (i.e., minimizing )
  (x10 less) have been achieved
  Warning: can lead to non-adiabatic emittance exchange
Limited by

## Slide 18: Emittance exchange SLS booster coupling resonance crossing
Minimize to reduce
too small for the resonance crossing speed
emittance don’t fully exchange
reduce crossing speed
crossing is slower but more complete
radiation damping starts to ruin emittances
Finding a good balance is difficult!
Boosters can suffer for tune-jitter from power supply timing jitter
What other ways can we do emittance exchange?

## Slide 19: Ways of doing emittance exchange Resonances in boosters + induced coupling

## Slide 20: Emittance exchange pulsed skew quadrupole
Step 1: achieve low value of and set
  no emittance sharing
Step 2: increase abruptly using a pulsed skew quadrupole
  emittances starts exchanging
Step 3: turn off skew quadrupole or extract beam when emittances are fully exchange
  Pulse-shape is (in the ideal case) not important
  Optimum emittance exchange: “pi-pulse”

## Slide 21: Emittance exchange pulsed skew quadrupole
0.29, 1
02
The detuning ( makes a perfect exchange impossible
  But detuning needed because
How to improve?
  Smaller and smaller
  Larger
Square-pulse for

## Slide 22: Emittance exchange pulsed semi-skew quadrupole
Idea by Peter Kuske: combine tune shift from pulsed quadrupole with coupling from pulsed skew quadrupole
Tune shift and most coupling is controlled by only one power supply
Only a modest quadrupole strength is needed (w.r.t. pure-skew quad)
The natural can be basically zero small before exchange gives small after exchange
Normal quadrupole
Skew-quadrupole 45° rotation
Semi-skew-quadrupole 22.5° rotation
Effect of quadrupole rotated rad = 22.5°:
(for )
+
=

## Slide 23: Emittance exchange pulsed semi-skew quadrupole
0.29 +
29 +
Note: same magnet strength as pulsed skew quadrupole example but smaller due to magnet rotation
Perfect exchange possible despite large detuning (
24

## Slide 24: Emittance exchange AC skew quadrupole
Emittance exchange through resonance crossing and the pulsed skew-quadrupole schemes requires to be small
Oscillating (“AC”) skew quadrupole can be used to excite the resonance with
  Condition:
Example:
Important observations
Arbitrary selection of tunes!
  best booster performance by picking optimum working point
  only affects frequency of AC skew quad
“Arbitrary” selection of
  small slow exchange larger effect of damping

## Slide 25: Conclusions
Emittance exchange is a way of improving horizontal off-axis injection from booster synchrotrons into low-dynamic aperture machines
The reduced may allow the re-use of existing boosters: saves dark time and money
Many exciting options!
  Transfer line exchange
  Coupling resonance crossing
  Pulsed- and AC-skew quadrupole
 | Emittance sharing | Coupling resonance crossing | Pulsed skew quadrupole | AC skew quadrupole | Transfer line exchange
Emittance exchange quality | 50% | 80-100% | 80-100% | 95-100% | 95-100%
Price tag | - | - | 💲 | 💲 | 💲💲
Space requirement | - | - | ⌂ | ⌂ | ⌂⌂
Operational stability | ☺☺ | (☹) | ☺☺ | ☺ | ☺☺☺
Technological requirements | - | (⚒) | ⚒⚒ | ⚒⚒⚒ | ⚒

## Slide 26: Thank you for your attention!

## Slide 27: Emittance exchange APS-U transfer line
Projected emittances tracked through APS-U transfer line with emittance exchange after skew quadrupoles 1-6.
0
1
1
2
3
6
4
5
2
3
4
5
6

## Slide 28: Emittance exchange Transfer line exchange errors
Calibration errors lead to non-perfect emittance exchange
Example: APS-U BTS exchange section
  Apply random relative error to quadrupoles of varying RMS value
  Calculate at end of exchange section
    = 0 perfect exchange
    = 1 no exchange
Results:
5% RMS calibration error on skew quadrupole strengths gives on average ~20% deterioration of emittance exchange
Warning: Not totally scientifically sound.
Use with caution!

## Slide 29: Resonance crossing: adiabaticity
Resonance crossing must be slow to allow for the emittance exchange: “adiabatic”
Crossing too quickly will lead to incomplete exchange: “non-adiabatic”
What is the impact of non-adiabaticity?
Define quality of emittance exchange:
Scaling parameter describing adiabaticity
Page 29

## Slide 30
Simulation emittance exchange in the SLS booster lattice with different and
  is indeed a good scaling parameter for adiabaticity
  gives good exchange
Landau-Zener formula from QM describes the scaling
Emittance exchange: adiabaticity
adiabatic
non-adiabatic

## Slide 31
Emittance exchange: damping
Radiation deteriorates the emittance exchange when beam is out of equilibrium
Effect of radiation in SLS booster: extracting after with
  Beam must be extracted early, but working point must be far away from resonance

## Slide 32
SLS booster decoupling
Vertical beam offsets in sextupoles lead to x-y coupling
Orbit in SLS booster is not corrected due to lack of available BPMs
  coupling may stem from vertical offsets, leading to vertical dispersion and emittance sharing
Minimizing in transfer line can lead to decoupling
  Closed orbit bumps
  Single-corrector optimization

## Slide 33
SLS booster decoupling
Works very well!
  Factor 2 reduction in
  Suppression of at BRTL cameras
  Factor 10 reduction in
better after emittance exchange