## Slide 1: Prognostic ParFlow integrated hydrologic model applications at stakeholder-scale over central Europe
CRC1502
DETECT
sfb1502.de
2025-03-17 I Klaus Goergen1,2, Alexandre Belleflamme1,2, Suad Hammoudeh1,2, and Stefan Kollet1,2
1Institute of Bio- and Geosciences (IBG-3, Agrosphere), Research Centre Jülich (FZJ), Jülich, Germany
2Centre for High-Performance Scientific Computing in Terrestrial Systems (HPSC TerrSys), Geoverbund ABC/J, Jülich, Germany
k.goergen@fz-juelich.de, https://www.fz-juelich.de/profile/goergen_k

## Slide 2: Integrated modelling of terrestrial systems group (S. Kollet)
ParFlow integrated hydrological model (github.com/parflow)
Physically based model, explicit representation of transport processes and feedbacks
2D/3D surface and subsurface hydrodynamics are treated in continuum approach
Land-atmosphere interactions through Common Land Model (CLM)
Consistent terrestrial water cycle representation
Our interest: Terrestrial water cycle functioning, interactions, feedbacks (G2A), and changes
Ground Surface
Water Table
Infiltration Front
Saturated Zone
Vadose Zone
Vegetation
Atmospheric Forcing
ECMWF
CLM
ParFlow
Integrated HM with 3D hydrodynamics
Added value of IHMs, e.g., due to: Redistribution of surface and groundwater, streamflow aquifer interactions, ponding / flowing water in convergence zones, evolution of river networks, km-scale heterogeneity, hill-slope processes
ParFlow overview: Kuffour et al. (2020, GMD)
Realistic process representation
Condon and Maxwell (2017, HESS)

## Slide 3: Prognostic ParFlow simulations for water resources
After 2018/2019 droughts: Setup DE06 in co-design approach with agriculture stakeholders for water resources
Careful setup of hydro-facies distributions and soil hydraulic properties
Extensive spinup
No calibration or tuning
DE06: “Hydrologic Germany”, 611m resolution, 2000x2000x15 grid points, to 60m depth w/ ParFlow/CLM
Van Genuchten parameters from ROSETTA
0-0.02m depth
42-60m depth
IGBP type land cover from CORINE USDA soil types from SoilGrids textures IHME hydrogeological types
Belleflamme et al. (2023, Frontiers in Water)

## Slide 4: System for daily DE06 quasi-operational monitoring/forecasting runs
Also available: HRES-driven climatology is from 2011, workflow is on JSC/JUWELS HPC GPU Booster
Daily forecast ensemble
+ 10 days
HRES = deterministic
ENS = 50-member, probabilistic
dn
dn+1
HRES
dn-1 h0-h24
HRES
dn h0-h24
ECMWF medium-range forecast
HRES – ENS01 – ENS02 … ENS50
dn h0-h240
dn-1
HRES
dn-2 h0-h24
ECMWF medium-range forecast
HRES – ENS01 – ENS02 … ENS50
dn+1 h0-h240
ECMWF seasonal predictions
SEAS01 – SEAS02 … SEAS50
dn h0-h5136 (7 months)
ParFlow/CLM
historical time series
combination of 24hr HRES forecast
ParFlow/CLM
medium-range forecasts every / 2nd day
ParFlow/CLM
seasonal predictions
every 3 months
Initial conditions
IC
IC
IC
Belleflamme et al. (2023, Frontiers in Water)
Every 3 months
+ 7 months
SEAS = 50-member, probabilistic
Dissemination
Portal for farming community
General public
interface
Data portal
Experimental Water Resources Bulletin

## Slide 5: Agriculture stakeholder information needs define our products
Towards a more weather extremes-resilient agriculture www.adapter-projekt.de
Plant available water 2023-07-25 daily mean, 0-30cm depth
Fraction of total PAW [%]
Capillary rise [mm/day] Seepage water
Groundwater
Seepage water / capillary rise 2023-07-25 daily sum, 30cm depth
e.g., water stress impacts
e.g., leakage of nutrients, GW recharge
e.g., 8+ diagnostics daily
Soil water saturation (end of day)
Subsurface water storage change (end of day)
Water table depth change (end of day)
Soil temperature in 5cm depth (daily mean)
Belleflamme et al., (2023, Frontiers in Water)
3x3km2 timeseries, including uncertainties

## Slide 6: Experimental Water Resources Bulletin (eWRB)
Seasonal predictions of subsurface water storage www.adapter-projekt.de/bulletin/index_en.html
Hindcast, deterministic ECMWF/HRES forcing
50-member seasonal forecast
Hydrometeorological extremes, recent severe droughts, well captured
Belleflamme et al. (under prep.), Hammoudeh et al. (under prep.)
2024-08
2022-09

## Slide 7: w/ DE06: Analyse unprecedented Central Europe 2021-07-14/15 flood
Sustained, intense, widespread rainfall from a quasi-stationary low
Rainfall event affected complete Eifel-Ardennes low mountain ranges drainage network
NWP models predicted July ‘21 precipitation extremes
Major natural hazard in north-western Europe (many casualties, high damages)
E.g., Ahr catchment:
  70mm July long-term mean,
  115mm/72h from 2021-07-12 to 14,
  100mm/12h during 2021-07-14 afternoon
Goal: Process-based analysis to demonstrate the prognostic capabilities of ParFlow/CLM DE06 ensemble
Erftstadt-Blessem, Erft www.welt.de
Schuld, Ahr www.focus.de
72h (-07-12 to 14) radar precipitation sum RADKLIM
missing
values
Domain subset: ≈150x150km2
Heavily affected catchments: Ahr, Vesdre, Kyll, Erft
Vesdre 669km2
Chaudfontaine gauge
Ahr 753km2
Altenahr gauge

## Slide 8: Dynamics and order of magnitude of discharge can be reproduced
Large precipitation bandwith leads to highly differing discharge peaks; same with QPEs from radar observations (Saadi et al., 2023)
Tuning, e.g., possible via streamflow parametrisations (Manning’s coefficient, but roughness unknown or not represented)
The DE06 water resources forecast “as is” captures extreme flood event w/o additional calibration / tuning
Use DE06 as-is for process analysis; no focus on forecast skill or an exact event reproduction
Goergen et al. (under rev.)
DE06 ENS41
DE06 HRES
Based on Parflow overland flow
ParFlow/CLM DE06
ECMWF HRES, ENS forcing
Initialisation: 2021-07-13_12UTC
Reconstructed: Qpeak=1000-1200m3s-1
at Altenahr (Roggenkamp Herget, 2022, HYWA); Qpeak=680m3s-1
at Chaudf. (pers. comm. Uni Lüttich)
Deteministic HRES
atmospheric forcing:
too low discharge
HHQpre21=236m3 s-1
HHQpre21=275m3 s-1
Discharge, Ahr river at gauge Altenahr
Discharge, Vesdre river at gauge Chaudfontaine
Highest discharge ensemble member

## Slide 9: The soil almost reached saturation during the event
Our interest is in the physical processes
No infiltration excess overland flow
Very low overland flow outside river channels
High exfiltration in the valleys
We hypothesize that there was a strong pressure response of the system
Vesdre: Different preconditioning; higher saturation at the onset
Maximum average soil saturation (0-30cm) over the 4 catchments is 91-97%
2021-07-12_01-24UTC, Mon 2021-07-13_01-24UTC, Tue 2021-07-14_01-24UTC, Wed 2021-07-15_01-24UTC, Thu
2021-07-13_00UTC, Tue 2021-07-14_00UTC, Wed 2021-07-15_00UTC, Thu 2021-07-16_00UTC, Fri
before after
Ensemble member:
Relatively homogeneous soil hydraulic properties between catchments

## Slide 10: Strong buffer effect through subsurface storage
Ahr catchment: Increase in subsurface storage mitigates stream flow response, despite 70% saturation (14.7. 00UTC)
Vesdre catchment: Initially higher saturation, less subsurface buffer, about all precipitation transformed into discharge
Due to surface and subsurface water interaction, dynamics is different than for flash floods (no infiltration excess overland flow)
Up to 1/3 of the precipitation can infiltrate in the Ahr catchment, avoiding even higher discharge peaks
Cummulative sums [mm h-1] of
mean precipitation,
total subsurface storage change, discharge per unit catchment area
DE06 ENS41
Ahr river
catchment
DE06 HRES
Vesdre river
catchment
Highest discharge ensemble member
Precipitation
Subsurface storage change
Discharge

## Slide 11: Conclusions and outlook
Use for water resources applications and hydrometeorological extreme events
Uncalibrated physics-based ParFlow IHM can capture dynamics and magnitude the July 2021 flood event
For the Ahr, the subsurface could absorb about 1/3 of the precipitation, mitigating the stream flow response
asdasd
Outlook
The physical representation of groundwater-surface water interactions affords hypothesis testing and will be used for more in-depth process analysis of the 2021 flood event
With new exascale JSC/JUPITER HPC a pan-European forescast domain (EU06) seems feasible
Combination of added value of ParFlow IHM and high-resolution atmospheric models in coupled ESMs
IHM ParFlow/CLM with DE06 setup is an applied, highly versatile monitoring and forecasting system