## Slide 1: Operational Hydrologic Ensemble Forecasts in Small Catchments – Implementing New Products for Precipitation Estimation and Seamless Predictions
Jens Grundmann & Michael Wagner
PrePEP Bonn // 18. März 2025
TU Dresden, Chair of Hydrology

## Slide 2
Introduction: HoWa-PRO
DWD + Uni Augsburg
TU Dresden
LHWZ + PIKOBYTES
!
Prob. Warning
User dialogue
Meteo. ensemble
forecast
Hydrologic
Ensemble Forecast
Zeit
Q
QPE with radar+CMLs
Small catchments and voluntary flood defence forces
Benefit?
Communication of uncertainties?
Suitable warning products?
Is there a benefit of upcoming new data products?

## Slide 3
Introduction: Saxony and pilote regions
Vogtland
Weiße Elster
Oelsnitz (328 km²)
Adorf 1 (170 km²)
Bad Elster (47,7 km²)
Osterzgebirge
Rote Weißeritz
Hainsberg 5 (160 km²)
Reichstädt (12.7 km²)
Dippoldiswalde (77.4 km²)
Schmiedeberg (53.7 km²)
Bärenfels (6.77 km²)
Lockwitzbach
Kreischa (22.9 km²)
Müglitz
Dohna (200 km²)
Lauenstein 4 (75.4 km²)
Geising (26.2 km²)
Oberlausitz
Mandau
Zittau 6 (277 km²)
Großschönau (161 km²)
Seifhennersdorf (74.9 km²)
Niederoderwitz (28.8 km²)

## Slide 4
Used data products of DWD for demonstrators
EFShowa
RadolanRW
RadolanRV
IconD2
IconD2EPS
IconEU
Radar data
Nowcast
Forecast
Prototypic Forecast
Legend
Data type Properties
EFSadv
pyRADMAN
INTENSE seamless ensemble now- to forecast
IconD2
Prototypic Data
Established Data

## Slide 5
Used data products of DWD for demonstrators
Product | Dx | dt | Update | Forecast horizon | Delivery offset
RadolanRW | ~1 km | 1 h | 30 min | - | 26 min
pyRADMAN | ~1 km | 15 min | 15 min | - | 6/11 min
RadolanRV | ~1 km | 5 min | 5 min | 2 h | 4 min
IconD2 | ~2 km | 15 min | 3 h | 48 h | 75 min
IconD2EPS | ~2 km | 15 min | 3 h | 48 h | 140 min
IconEU | ~4 – 7 km | 1 – 6 h | 3 – 6 h | 48 – 120 h | 230 min
INTENSE | ~2 km | 15 min | 0.5 – 2 h | 12 h | 25 min
Example Lauenstein@Müglitz (Osterzgebirge)
EFShowa (radRW, radRV, IconD2EPS)  radRW, updated each 30 min
EFSadv (pyRADMAN, INTENSE, IconD2)  pyRADMAN, updated each 15 min
blue | Measured values
green | Nowcast
blue | Forecast
red | seemless forecast

## Slide 6
Operational hydrologic Ensemble Forecast System (hydEFS)
FloodSentinel
Data
Radar
Radolan RW
pyRADMAN
Nowcast
Radolan RV
Radvor RQ
Forecast
ICON-D2(-EPS)
ICON-EU(-EPS)
Seamless
Sinfony INTENSE
Q (runoff)
Automatic retrieval, partly converted to NetCDF
OSW-API
Control
Sentinel
Criteria exceedance in domain
Time
Time step
Criteria type
Domain
Region (gauge, node)
Hyd. Model
Counter
…
Analysis
WeatherDataAnalysis (time, domain)
New products
Forecast persistence
Forecast quality
HYDforecast analysis (time, region)
Criteria exceedance in region
Standardized Output
HYDforecast (time, time step, region, model, counter)
Model: DeHM, KiWaNA
Preprocessing
Simulation (ensemble)
Postprocessing
yes
Visualization
SentinelVisualizer
Timeseries
Persistence
Comparison
Visualization
Rest-API
Web Demonstrator
WeatherDataHarmonizer (time step, spatial resolution, coverage, format)
yes
Standardized Precipitation
weatherDataHarmonizer
https://gitlab.hrz.tu-chemnitz.de/ihmtud/weatherdataharmonizer/

## Slide 7
Web-demonstrators – EFShowa & EFSadv
Web-demonstrators
Rainfall exceedance probability
Rainfall amounts (quantiles)
Expected runoff (quantiles & thresholds)
Easy to read flood warning
http://howa-innovativ.hydro.tu-dresden.de/WebDemoLive/
http://howa-innovativ.hydro.tu-dresden.de/WebDemoEFSadv/
EFShowa
EFSadv

## Slide 8
Demonstrator – howapro.de
Warning application https://howapro.de
More modern design and UI
Regional overview
Hydrographs for real and virtual gauges
Archive and API
Used for trainings
Useable on smart phones
https://howapro.de

## Slide 9
Evaluation
Operationel ensemble forecast: 13.09. – 16.09.2024 in Lauenstein@Müglitz
Impact of controled flood reservoir
EFSadv
EFShowa

## Slide 10
Runoff at gauges & mean areal rainfall of catchments  quantiles and forecast horizons
th1 |  | sim | 
 |  | true | false
obs | true | tt | tf
 | false | ft | ff
POD: probability of detection
FAR: false alarm ratio
Evaluation
Area Under Curve (AUC) – Theorie
+ other metrics based on contingency table (e.g. ACC, CSI, f1, …)
and goodness-of-fit indicators (e.g. KGE, NSE, nRMSE, ….)

## Slide 11
Evaluation – Ensemble over period (01.12.2023 – 31.12.2024)
Mean areal rainfall of catchments
EFShowa: 5152 forecasts
EFSadv: 5032 forecasts  ~29 % of potential forecasts
Mean areal rainfall
  Observation: RadolanRW
  dt = 3 h sum
  main run, median, 25%-, 75%-quantiles
AUC
KGE
west
middle
east

## Slide 12
Evaluation – Ensemble over period (01.12.2023 – 31.12.2024)
Runoff at gauge stations
EFShowa: 5152 forecasts
EFSadv: 5032 forecasts  ~29 % of potential forecasts
Runoff
  Observation: Gauge
  dt = 1 h
  main run, median, 25%-, 75%-quantiles
AUC
KGE
west
middle
east

## Slide 13
Evaluation – Event based (17.–21.8.2024)

## Slide 14
Evaluation – Event based (17.–21.8.2024)
Mean areal rainfall
18.08. 01:30
04:15
07:30
10:30
13:30
16:30
19:30
22:30
19.08. 01:15
04:30
observed
18.08. 01:15
04:15
07:15
10:15
13:15
16:15
19:15
22:15
19.08. 01:15
04:15
observed
EFSadv
EFShowa
Max intensity

## Slide 15
Conclusions
Hydro-meteorologic ensemble forecasts allow for flood early warning
FloodSentinel: scalable ensemble forecast system for small catchments
Web-demonstrators with established and prototypic precipitation data of DWD since mid/end 2023 (ESFhowa & ESFadv)
EFSadv: earlier delivery, frequent updates, forecasts starts with ensemble
Evaluation over period: benefits of EFSadv for first forecast hours depending on region (decreasing from west  east)
Evaluation event based: better timing of EFSadv visible
Evaluation of runoff forecasts depends on quality of hydrologic model  check with regional AI-model
Next Steps
Evaluation: longer period with more extremes, additional metrics e.g. CRPS(S)
Combination of INTENSE with IconD2EPS – longer forecast horizon
west
middle
east