## Slide 1
DEVELOPMENT OF A CONTROL SYSTEM FOR THE STABILIZATION OF SYNCHROTRON X-RAY BEAMS
NICCOLÒ LA ROSA
ENG. SAMUELE MOSCATO
DEPARTMENT OF ELECTRICAL, ELECTRONIC, AND COMPUTER ENGINEERING
PROF. MAIDE BUCOLO
DR. MASSIMO CAMARDA
PhD in Energy, Computer and Telecommunications Systems Engineering

## Slide 2
SYNCHROTRON CONTROL SYSTEMS OVERVIEW #1
LAB- REPLICA #2
OPEN-LOOP SYSTEM #3
  IDENTIFICATION OF THE PROCESS MODEL
CLOSED-LOOP CONTROL SYTEM WITHOUT DISTURBANCE #4
  PID TUNING
CLOSED-LOOP CONTROL SYSTEM WITH DISTURBANCE #5
  EXPERIMENTAL RESULTS
CONCLUSIONS AND OUTLOOKS #6
TABLE OF CONTENTS

## Slide 3
CONTROL OVERVIEW
#1

## Slide 4
ORBIT FEEDBACK SYSTEM (GOFB)
BEAMLINE CONTROL SYSTEM
SLOW ORBIT FEEDBACK SYSTEM
FAST ORBIT FEEDBACK SYSTEM
(FOFB)
(SOFB)
CONTROL OVERVIEW
#1

## Slide 5
ORBIT FEEDBACK SYSTEM (GOFB)
BEAMLINE CONTROL SYSTEM
CONTROL OVERVIEW
#1
Electron beam stabilization
Closed Loop Gain Bandwidth ≈ 300 Hz
FPGA Based Architecture
Closed Loop Gain Bandwidth < 10 Hz
Software Based Architecture (Tango – EPICS ecc..)
Radiation beam stabilization
Monitoring and real time data acquisition

## Slide 6
CONTROL OVERVIEW
Mechanical Actuation
#1

## Slide 7
CONTROL OVERVIEW
Electrical Actuation
INSERTION DEVICE
#1

## Slide 8
CONTROL OVERVIEW
Electrical Actuation
INSERTION DEVICE
ACTUATION
+
CONTROL
SENSING
BEAM SOURCE
#1

## Slide 9
Analog Oscilloscope
Hamamatsu S5980
LAB-REPLICA
  Generates an electron beam thanks to the Cathodic Ray Tube (CRT).
  Sensitive to magnetic fields (used for disturbance).
  Sensitive to electric fields (used for actuation).
  2 X 2 matrix of photodiodes.
  Visible-light sensitive.
  Structurally Equivalent to the state-of-art sensors (like SenSiC ones, but in Silicon and non-transparent..)
#2

## Slide 10
Electromagnet
Buffer Amplifier
  Disturbance source.
  Generates a magnetic field which deflects the beam inside the CRT.
  Decoupling effect.
  Allows to supply the electromagnets, avoiding overload risks.
LAB-REPLICA
#2

## Slide 11
STM32 NUCLEO-H723ZG
PCR4
  Two Digital-to-analog converters (DACs).
  Ensures a higher data exchange rate through SPI protocol.
  4-channel with 24-bit of resolution and sampling rate up to 54 kHz.
  Nominal resolution of 3fA in the range of ±25 nA.
LAB-REPLICA
#2

## Slide 12
OPEN-LOOP REPLICA SYSTEM
TRIGGER
#3

## Slide 13
EXPERIMENTAL PROCESS IDENTIFICATION
Steady-State Analysis
#3

## Slide 14
EXPERIMENTAL PROCESS IDENTIFICATION
Steady-State Analysis
#3

## Slide 15
EXPERIMENTAL PROCESS IDENTIFICATION
Transient Analysis
Latency
#3
860 ms

## Slide 16
CLOSED-LOOP CONTROL SYSTEM
PID Controller
Model
#4

## Slide 17
CONTROL IMPLEMENTATION IN SIMULATION
ZIEGLER-NICHOLS PID TUNING RULES
COHEN-COON PID TUNING RULES
PID Controller
Model
Reference
#4

## Slide 18
CONTROL IMPLEMENTATION
IN SIMULATION
#4

## Slide 19
CONTROL IMPLEMENTATION
IN LAB-REPLICA
CONTROL: OFF
CONTROL: ON
CONTROL: OFF
CONTROL: ON
#4

## Slide 20
PID EXPERIMENTAL TUNING
#4

## Slide 21
Disturbance
SPI Communication frequency: 10 kHz
Control Action
[ 10,100,1000 Hz]
Limited by low signals (nA) generated by the sensor
#5
CLOSED-LOOP CONTROL SYSTEM WITH DISTURBANCE

## Slide 22
Disturbance
#5
CLOSED-LOOP CONTROL SYSTEM WITH DISTURBANCE

## Slide 23
CLOSED-LOOP CONTROL SYSTEM WITH DISTURBANCE
Disturbance
#5

## Slide 24
CONTROL IN PRESENCE OF DISTURBANCE 100 Hz
Rise Time ≈ 0.04 sec
CONTROL: OFF
CONTROL: ON
DRIFT : 0.11 mm/sec
‘IMPULSE’ > 200 mm/sec
#5

## Slide 25
CONTROL IN PRESENCE OF DISTURBANCE
Rise Time ≈ 0.15 sec
Rise Time ≈ 0.04 sec
Rise Time ≈ 0.014 sec
CONTROL: OFF
CONTROL: ON
CONTROL: OFF
CONTROL: ON
CONTROL: OFF
CONTROL: ON
DRIFT : 0.11 mm/sec
DRIFT : 0.11 mm/sec
DRIFT : 0.11 mm/sec
10Hz
100Hz
1 kHz
#5

## Slide 26
CONCLUSIONS AND OUTLOOKS
Closed-Loop Control System successfully designed and implemented both in simulation and in real world.
Validation of the robustness of the systems in presence of drift disturbances.
Period at PSI for developing novel control solutions (whitebeam monitoring?)
Currently developing a “new replica” and its control system using a mechanical actuation.
17-23 June: Beamtime at SOLEIL (Galaxies) . (Mechanical Actuation)
#6
Eurostar Project

## Slide 27
THANK YOU